## Slide 1: RHESSys history, community, & processes
Lin and Band, Aug 2020

## Slide 2: RHESSys (brief) history
RHESSys (Regional Hydro-Ecological Simulation System) is a GIS-based, terrestrial ecohydrologic modeling framework designed to simulate carbon, water and nutrient fluxes at the watershed scale. RHESSys models the temporal and spatial variability of ecosystem processes and interactions at a daily time step over multiple years by combining a set of physically based process models and a methodology for partitioning and parameterizing the landscape.
Band 1989, Band and Wood 1988
slope
aspect
accumulative drainage area
Hillslopes
stream network
Watershed delineation
Elevation ->

## Slide 3: RHESSys (brief) history
RHESSys (Regional Hydro-Ecological Simulation System) is a GIS-based, terrestrial ecohydrologic modeling framework designed to simulate carbon, water and nutrient fluxes at the watershed scale. RHESSys models the temporal and spatial variability of ecosystem processes and interactions at a daily time step over multiple years by combining a set of physically based process models and a methodology for partitioning and parameterizing the landscape.
Band 1989, Band and Wood 1988
Band 1991; Band et al., 1991
Incorporated MT-CLIM to extrapolate the base station climatic data according to elevation, aspect, and gradient through the surrounding complex terrain
Couple Forest_BGC with geographic information processing -> spatial pattern of ET and NPP
Precipitation -> snowpack
-> soil water
-> canopy interception
-> through fall
-> snowmelt water
Canopy photosynthesis based on [CO2], radiation, temperature, LAI, canopy conductance, day length
ET
PSN
ET
PSN
ET
PSN
Climate
Climate
Climate

## Slide 4: RHESSys (brief) history
RHESSys (Regional Hydro-Ecological Simulation System) is a GIS-based, terrestrial ecohydrologic modeling framework designed to simulate carbon, water and nutrient fluxes at the watershed scale. RHESSys models the temporal and spatial variability of ecosystem processes and interactions at a daily time step over multiple years by combining a set of physically based process models and a methodology for partitioning and parameterizing the landscape.
Band 1989, Band and Wood 1988
Band 1991; Band et al., 1991
Band, Patterson, Nemani, & Running, 1993; Nemani, Running, Band, and Peterson, 1993
MT-CLIM
Forest-BGC (Running and Coughlan, 1988)
TOPMODEL Beven and Kirby, 1979
ET
PSN
ET
PSN
ET
PSN
Climate
Climate
Climate
Lateral redistribution of resources

## Slide 5: RHESSys (brief) history
RHESSys (Regional Hydro-Ecological Simulation System) is a GIS-based, terrestrial ecohydrologic modeling framework designed to simulate carbon, water and nutrient fluxes at the watershed scale. RHESSys models the temporal and spatial variability of ecosystem processes and interactions at a daily time step over multiple years by combining a set of physically based process models and a methodology for partitioning and parameterizing the landscape.
Band 1989, Band and Wood 1988
Band 1991; Band et al., 1991
Band, Patterson, Nemani, & Running, 1993; Nemani, Running, Band, & Peterson, 1993
Band, Mackay, Creed, Semkin, & Jeffries, 1996; Creed, Band, Foster, Morrison, Nicolson, Semkin, &Jeffries, 1997; Mackey and Band, 1997; Lammers et al. 1997

## Slide 6: RHESSys (brief) history
RHESSys (Regional Hydro-Ecological Simulation System) is a GIS-based, terrestrial ecohydrologic modeling framework designed to simulate carbon, water and nutrient fluxes at the watershed scale. RHESSys models the temporal and spatial variability of ecosystem processes and interactions at a daily time step over multiple years by combining a set of physically based process models and a methodology for partitioning and parameterizing the landscape.
Band 1989, Band and Wood 1988
Band 1991; Band et al., 1991
Band, Patterson, Nemani, & Running, 1993; Nemani, Running, Band, & Peterson, 1993
Band, Mackay, Creed, Semkin, & Jeffries, 1996; Creed, Band, Foster, Morrison, Nicolson, Semkin, &Jeffries, 1997; Mackey and Band, 1997; Lammers et al. 1997
Band, Tague, Brun, Tecenbaum, & Fernandes, 2000; Tague and Band, 2001; Band, Tague, Groffman, & Belt, 2001; Tague and Band, 2001b
Distributed Hydrology Soil Vegetation Model (DHSVM) Wigmosta, Vail, & Lettenmaier, 1994
N cycling and export
Event controls (tecfiles)

## Slide 7: RHESSys catchments
Information provided by Naomi Tague [https://tagueteamlab.org/portfolio/where-is-rhessys-being-used/]

## Slide 8: RHESSys community

## Slide 9: RHESSys coding community
One of the branches that is adapted to East Coast environments and projects
Refining hydrology and ecosystem interactions
Improving model for urban catchments
Making technical improvements

## Slide 10
RHESSys

## Slide 11
RHESSys

## Slide 12
RHESSys
Header file
Worldfile

## Slide 13
RHESSys
Flowtable

## Slide 14
Patch
Surface water (detention)
Precipitation
Canopy interception
Throughfall
Hillslope GW
Rooting depth
Transpiration
RZ water (RZ storage)
Evaporation
litter interception
Returnflow
FC
Cap. Rise
Drainage
Intermission water (unsat storage)
(unsat FC)
(rz FC)
Soil depth
Infiltration
(Rz Drain)
(Unsat Drain)
Unsaturation Zone
GW2Riparian
Daily precipitation comes from zone and station time series
A fixed sized canopy store to hold canopy interception
Throughfall to non-fixed sized surface detention
Water holding capacity is within surface detention
  Litter interception
  Urban impervious surface water detention
Detention - Litter interception is subject to infiltration
Detention - Litter interception - infiltration is subject to surface lateral transport
Rain intensity
Soil vertical conductivity
infil. = Precip * (1-%imp.)
<
Rain intensity
Soil vertical conductivity
>
This runs in daily; it will be balanced by return flow, drainage, and lateral transport

## Slide 15
Patch
Surface water (detention)
Precipitation
Canopy interception
Throughfall
Hillslope GW
Rooting depth
Transpiration
RZ water (RZ storage)
Evaporation
litter interception
Returnflow
FC
Cap. Rise
Drainage
Intermission water (unsat storage)
(unsat FC)
(rz FC)
Soil depth
Infiltration
(Rz Drain)
(Unsat Drain)
Unsaturation Zone
GW2Riparian
Unsaturation zone is partitioned into two zones:
  “Root zone” (a fixed depth, e.g., 0.6 - 1 m)
  Intermission zone (may not exist if water table rises)
Vegetation can access water within the “root zone”
Unsaturation Soil water = root zone water + intermission zone water
unsaturation Soil water > FC(water table depth) -> drainage (from unsaturation to saturation zones)
unsaturation Soil water < FC(water table depth) -> capillary rise (from saturation to unsaturation zones and distributed to root zone and intermission zone
Saturation zone was used be assumed bottomless or very deep but is now bounded by a spatially distributed finite soil depth (extracted, interpolated, and calibrated)
RHESSys also has snowpack accumulation and melting processes but not mentioned or graphically represented here

## Slide 16
Patch
Surface water (detention)
Precipitation
Canopy interception
Throughfall
Hillslope GW
Rooting depth
Transpiration
RZ water (RZ storage)
Evaporation
litter interception
Returnflow
FC
Cap. Rise
Drainage
Intermission water (unsat storage)
(unsat FC)
(rz FC)
Soil depth
Infiltration
(Rz Drain)
(Unsat Drain)
Unsaturation Zone
GW2Riparian
Fracture flow (from near surface to GW); gw1 (0 - 0.2)
A new gw3 (0 - 0.2) calibration parameter is added to described the leaching from the bottom soil column to GW
Outflow from GW could be at basin outlet as part of streamflow or discharge into the unsaturation zone at the cove area (likely riparian area); required “riparian” setting in the flow tables and -gw2riparian flag in the command line
Prop. of water cannot drain out

## Slide 17
Patch
Precipitation
Canopy interception
Throughfall
Hillslope GW
Rooting depth
Transpiration
RZ water (RZ storage)
Evaporation
Returnflow
FC
Cap. Rise
Drainage
Intermission water (unsat storage)
(unsat FC)
(rz FC)
Soil depth
Infiltration
(Rz Drain)
(Unsat Drain)
Unsaturation Zone
GW2Riparian
Porosity profile
Conductivity
Lateral transport
Transmissivity
Prop. of water cannot drain out
Surface water (detention)
litter interception
Poros = space in soil column that can hold water
Poros space may or may not be uniform in the soil column; Porosity profile
Other soil characters:
  Saturation conductivity -> transmissivity, infiltration, drainage, cap.rise
  Porosity -> sat.deficit
  Texture; %sand, %clay, and %silt -> denitrification and nitrification
  Organic matter content -> decomposition, immobilization, mineralization
  Pore size index -> FC, transmissivity, cap.rise
  Psi air entry -> FC, transmissivity, cap.rise
  Thickness of horizon B and C -> active zone depth for denitrification and nitrification
  Adsorption for solutes -> solute lateral transport

## Slide 18
Patch
Precipitation
Canopy interception
Throughfall
Hillslope GW
Rooting depth
Transpiration
RZ water (RZ storage)
Evaporation
Returnflow
FC
Cap. Rise
Drainage
Intermission water (unsat storage)
(unsat FC)
(rz FC)
Soil depth
Infiltration
(Rz Drain)
(Unsat Drain)
Unsaturation Zone
GW2Riparian
Porosity profile
Conductivity
Lateral transport
Transmissivity
Prop. of water cannot drain out
Surface water (detention)
litter interception
Saturation lateral transport
  Gradient of water table
  Distance (between patches)
  Perimeter (DHSVM)
  Water table depth (sat_def_z)
  Conductivity profile
  Porosity profile

## Slide 19
RHESSys + stream model (Lin et al. 2015)
Decomposition in RHESSys
Canopy growth in RHESSys

## Slide 20
RHESSys (Lin et al. 2015)

## Slide 21
Canopy growth in RHESSys (based on BiomeBGC)

## Slide 22
Decomposition in RHESSys based on CENTURY model

## Slide 23
Developing for urban catchment

## Slide 24
Ponds (~ 1 m deep)
20 km2 Bolin, Chapel Hill, NC
Ponds
No ponds
Yes ponds

## Slide 25
Ponds and Detention ponds
Surface water (detention)
Precipitation
Canopy interception
Rooting depth
Transpiration
Evaporation
litter interception
Returnflow
FC
Cap. Rise
Drainage
Soil depth
Infiltration
Soil depth
Returnflow
Infiltration
Drain from top
Drain from bottom
Drain from some depth
(add more pond settings)
(drainDepth)
(max drain rate)
Detention pond designed drainage
(permeable bottom)

## Slide 26
Sanitary sewer

## Slide 27
(disconnected) Rooftops -> adjacent previous areas (e.g., lawns and rain gardens) (low-impact development; LID)
(connected) Rooftops -> storm sewers
Surface routing
Quick flow
Use GIS to identify the transfer from A to B
Define transfer rate
Engineering stormflow patterns

## Slide 28
Irrigation
Septic
Water sources
Surface pond
Groundwater
Current Patch - surface
Current Patch - subsurface (UNSAT)
Implementation
Flow table
actionCode 13 (irrigation)
In the neighbor rows:
drainIN patches
In the current patch:
patch
zone
hill
float: X (useless)
float: Y (useless)
float: Z (useless)
int: 1 (useless)
basement_depth
drainage_type (x 13)
total_gamma
# of drainTO neighbors (not include “road” if drainage_type =2) (not include irrigation sources)
Change to “-# of drainIN neighbors”
“road” patch
drainTO patches
patch
zone
hill
width
patch
zone
hill
Max daily withdrawal rate
Proportion of withdrawal from surface [0-1]
Proportion of withdrawal from this drainIN patch [0-1]
patch
zone
hill
gamma fraction
shared perimeter / dist
shared perimeter
Withdraw water from somewhere from surface or deep underground
Release the withdrawn water to somewhere else on surface or in subsurface
Rain garden / irrigation
Septic systems